## Slide 1: A 90nm CMOS Data Flow Processor Using Fine Grained DVS for Energy Efficient Operation from 0.3V to 1.2V
Saad Arrabi, Yousef Shakhsheer, Sudhanshu Khanna, Kyle Craig, John Lach, Benton Calhoun
University of Virginia
Background
Panoptic DVS (PDVS) Features
Additional PDVS Features
Fine temporal granularity
  Single clock cycle VDD-switching
  Utilize any slack for each clock cycle
Fine spatial granularity
  Each component can be assigned to a voltage independently
  Each DVS block does not require its own DC-DC converter
Efficiency
  VDD-switching breakeven energy of only a few cycles
  Capable of rapidly switching between high performance and ultra-low power sub-VT modes
Testing Infrastructure
Testing Methodology
Test Chip Design and Blocks
Test Results
Application challenges
  Battery life vs. battery form factor
  Variable performance demands
Previous work
  Single-VDD
  Multi-VDD
  Dynamic Voltage Scaling (DVS)
Limitations of previous DVS work
  Expensive to switch VDD with DC-DC converters (10s µsecs)
  VDD control only for large blocks
Our design (PDVS) goal
  Function efficiently across and switch efficiently between multiple power-performance modes
Our design features
  Fine temporal granularity
  Fine spatial granularity
32kb Data Memory
40 kb Instruction Memory
Control
VDDH VDDM VDDL
*
x4
Lvl. Conv.
VDDH VDDM VDDL
+
x4
x8
General Purpose
32b
Coefficients
x15
32b
Register Bank
Crossbar
160
32
PDVS data path
Multi-VDD data path
Single-VDD data path
Sub-threshold PDVS data path
VDDH
+
+
VDDH VDDM VDDL
+
+
+
e.g.
e.g.
Pipelined sensing scheme: Read access has a latency of 2 cycles but only a single cycle throughput. Pipelining enables lowering cycle time.
Clock
Wordline Enable
Sense Amplifier Enable
Read # 1
Droop Dev
Read # 2
Droop Dev
Sense Amplifier Output
Read # 1
SA Strobe
Data # 1 valid at SRAM output
Read # 2
SA Strobe
Data # 1 used
ModelSim Output
Cadence ADE Output
Logic Analyzer Output
Feature | This Chip
Process | 90nm CMOS Bulk w/ Dual VT
Area | 4.3mm x 3.3mm
Transistors | ~2 million
VDD | 250mV – 1.2V
SRAMs | 40kb & 32kb
PDVS
MVDD
Sub VT
SVDD
Inst Memory
Data Memory
VCO & Inst Block
3.3mm
Multiplier
Adder
Headers for the multiplier
Headers for the adder
4.3mm
Arithmetic components
  4 - 32b Kogge Stone adders
  4 - 32b Baugh Wooley multipliers
Input register
  16 - 32b registers 2 per arithmetic component
Registers for moving data
  8 - 32b general purpose registers
Constant registers
  15 - 32b registers programmed at setup
Clock system
  Internal voltage controlled oscillator (VCO)
  Countdown register to run pre-determined number of clock cycles
  External clock for controllable/slow frequencies
Branch system
  Loops
  Conditional and non-conditional jumps
Program counter
Single-VDD (SVDD)
Multi-VDD (MVDD)
Our design – Panoptic DVS (PDVS)
FPGA Board (left) and Mother Test Board (right) designed and used for the PDVS project. FPGA Board provided flexibility and ease of testing.
SRAM
Unified testing diagram
Test benches
(Synthesizable VHDL)
VHDL
Spectre
Silicon HW
Stimulus Generation
Xilinx FPGA
Functional
Verification
&
Measurement
Processor Model
Power
Performance
Higher performance for
slightly more power
Lower power for same performance
Four copies of the same data path
  SVDD, MVDD, PDVS, Sub-VT
Shared Instruction Memory and Data Memory
Shared control signals
Separate voltage rails for measurements
VCO clock for fast frequency
Reusable FPGA board
  Provides flexible interface
Separate voltage supplies
  Increases measurement accuracy
Hard-wired test program
  Tests the functionality of the data path
Scan chain the registers
  To read and write the registers at any cycle
Configurable delay memories
  Adapts the memory to the chip frequency
Memory bypass registers
  An alternative to memory to ensure functionality
Configurable clock system
  Enables slow external clock or fast internal VCO clock
  Runs specified number of clock cycles
Real-time probe
  Observe in real-time one of the registers
This Chip
Data Path Features
Control Block
Size | 40kb Instruction Memory; 32kb Data Memory
Bit-cell | 6T SRAM
Bank Size | 256x32
Fmax | 1GHz @ 1.2V
High speed operation
  1GHz read with high density bit-cell
  Pipelined Sensing enables high speed read operation
Pipelined sensing
SRAM read access
  Cycle 1: Decode and bit-line droop development
    Cycle 2: Sense amplifier enable and resolution
SRAM is accessed every cycle; Latency is not an issue
Circuit level implementation
    Uses a voltage latching sense amplifier (SA)
    The SA inputs are connected to the bitlines only when wordline enable is asserted
    Rising edge of the SA enable for a given operation is controlled by the next clock period’s rising edge, thereby pipelining the sensing
Adder/Multiplier
Measured normalized energy-VDD plot of a 32b Kogge Stone adder and a 32b Baugh Wooley multiplier. This plot was used for scheduling operations in the benchmarks.
Sub-Threshold
Time
Dithering
Benchmark Benefits
Change in average power & instantaneous power as the workload changes over time. Power waveform shows dithering between two rates to achieve an intermediate rate, resulting in near optimal average energy.
Simulated delay and energy of a 32b Kogge Stone adder at 0.3 V. Adder and header bulk (Adder,Header) are tied to VDDH (H) or to the virtual VDD rail (V).
Measured energy benefit (including overhead) of PDVS & MVDD vs. SVDD for single function single rate (SFSR) & single function multi rate (SFMR) at 67% and 50% rates with constant area for multiple benchmarks.
Dithering
  Block operates at two or more discrete power-performance modes to approximate the optimal energy at a given workload
Adaptability to workload
  As workload changes, voltage on data-path components can be dithered
  Utilize slack as processor is used across varying workloads
Near optimum performance
  Efficient switching and dithering achieves near-optimum energy results over multiple data flow graphs
Scan chain was used to read and write to all the registers on chip
Programs used for testing
  Cadence, Modelsim, Xilinx and custom Perl & Matlab programs
Models of the chip
  VHDL
  Spectre
Test benches
  The same test benches are run through each model and on hardware for functional verification
Test programs
  Various complexity of test programs, ranging from tests exercising small portions of the chip to full benchmarks
Hard-wired program was used as a fail-safe mechanism. Each adder accumulates by 1 and each multiplier multiplies the adder output by 3.
The chip, during hardware testing, was able to operate at super-threshold, drop to 250 mV, and then return to super-threshold.
Normalized Workload
Normalized Energy
Normalized Workload
Normalized Energy
Flow chart of the testing plan
Voltage (V)
Normalized Energy
SFSR (100% rate)
67% rate
50% rate
Time
Energy Savings
Energy Savings
Energy Savings
This work was funded in part by a DARPA seedling grant
VDDH VDDM VSUBVT
Virtual VDD
VSUBVT
VDDH
High VT
Level Converter & Body Connections